## Slide 1: Improvements in TECHNICAL projects
Manikandan Raju

## Slide 2: MuLTI-APPLICATION HIL TEST BEnch
Steering Angle Sensor S100
HIL Simulator
Steering ECU (Electric)
Body Control ECU
(Electric)
Vehicle Speed Sensor S302
Steering ECU (ICE)
Vehicle Speed Sensor S301
Body Control ECU (ICE)
Steering Torque Sensor S200
Steering Angle Sensor S101
Steering Torque Sensor S201
Plugin connector
Y connections to common I/O Pins
Separate connections to unique I/O Pins
DS 6101 Multi IO Board
Digital In/Out (PWM)
Analog In/Out
Resistor Simulation
Engine Simulation

## Slide 3: DEMO – MULTI APP HIL TEST BENCH (EPAS)
Configuration Desk
Simulink Model (Open/Closed loop)
Signal Chain
Port Connection

## Slide 4: Integration of dspace and vector tools via com api
COM API
Importing win32com client module in python scripts
CANoe Application is opened with COM API
Loading CANoe Configuration with databases, CAPL program nodes and Test modules.
Starting the measurement analysis and CAPL Test module Testcases are executed.
CANoe System Variables could be accessed and set by Automation desk python scripts.
Stopping the measurement in CANoe.
Test Results are generated and exported and also could be passed to Automation desk.

## Slide 5: DEMO - Integration of dspace and vector tools via com api
Automation desk Python Script with COM API
CANoe Application loading and running Test modules
COM API

## Slide 6: Syncing HIL MEASUREMENT DATA WITH Cycle TIME
Chart: Raw Measurement Data
Chart: Synced Measurement Data with regular cyccle time
HIl/SIL
Meas Sync Script
Measurement File
Test Automation

## Slide 7: DEMO - Syncing HIL MEASUREMENT DATA WITH Cycle TIME

## Slide 8: MuLTI-APPLICATION HIL TEST Bench
HIL Simulator
HIL Simulator
Steering Angle Sensor S100
Steering ECU E001
Vehicle Speed Sensor S301
Body Control ECU E101
Steering Torque Sensor S200
Steering ECU E002
Steering Angle Sensor S101
Steering Torque Sensor S201
Body Control ECU E102
Vehicle Speed Sensor S302